## Slide 1: Robotic Exploration for Mapping: Systems and Algorithms
PhD Candidate: Hao Men PhD Advisor: Professor Kishore Pochiraju
Committee: Professor David J. Cappelleri
Professor George Kamberov
Professor Souran Manoochehri
Professor Yan Meng
Design and Manufacturing Institute
Department of Mechanical Engineering Stevens Institute of Technology
March 28th, 2012
Doctoral Dissertation

## Slide 2: Overview
Introduction to robotic mapping & exploration
Research objectives
Robotic exploration and mapping process
System: Remotely Operated Autonomous Mapping System
Color point cloud processing and registration
  Point cloud analysis
  Color point cloud segments coarse registration
  Hue Assisted Iterative Closest Point Algorithm for fine registration
Path planning strategy for exploration
Conclusions
Future Works

## Slide 3: Introduction: Map
Map is a static visual representation of an area to symbolically describe dimensions and relationships between elements of specific space such objects, regions and themes [S. Thrun 2002].
Map of large underwater features, NOAA
Map of EU population distribution
Map of Hoboken, USGS
Stevens Campus 3D Map
Building 2D Drawing
Hudson Highlands State Park Topological Map
Notes: What is map? Why map is important?
NOAA=National Oceanic and Atmospheric Administration
Dimension accurate
Replace the google map with Stevens Campus 3D Map?

## Slide 4: Introduction: Map Construction
Carry ranging devices to measure object surface dimensions.
German Aerospace Center Airborne Synthetic Aperture Radar(SAR)
NASA Space Shuttle Radar Topography Mission
Urban surveying
Underwater Archaeology Mapping
Notes: theodolite

## Slide 5: Robotic Mapping
Utilize a robotic platform to carry the mapping device to explore an area and generate the complete map.
Saves mapping costs.
Decreases time consumption.
Work in hazardous environment.
Urban surveying, S. Thrun, 2004
Search & Rescue, M. Montemerlo, 2004
Mine mapping, S. Thrun, 2003
Underwater mapping, S. Williams, 2001
Notes: Mention Earthquake Tsunami and nuclear radial leakage .
Add carnegie building 2nd floor 40 pos map.
* Why need robotic mapping

## Slide 6: Research Objective
Objective Autonomously explore and generate a global 3D color point cloud map about a given area with no pre-known knowledge and positioning sensor.
System
  A mobile mapping robot to generate 3D color point cloud maps .
Process
  Create a adaptive exploration and mapping process in unknown urban environment.
Algorithms
  Point cloud analysis
    Occlusion detection, noise filtering, normal extraction, subsampling
  Color point cloud map registration
    Register maps generated at different positions into global frame.
  Exploration strategy
    Navigate robot to next best vantage position to compensate occlusions.
Notes: Objective of robotic mapping

## Slide 7: State of the Art
Systems
  Different mapping devices have been introduced for accurate map generation and localization.
    Sonar (S. Williams, 2001)
    Multiple 2D laser ranger(M. Montemerlo, 2004)
    Camera (J. Neira, 2008)
T. Peynot, 2004
M. Montemerlo, 2004

## Slide 8: State of the Art
Process
  Simultaneous Localization and Mapping (SLAM) methods to complete mapping from different scan segments . (J.A. Castellanos, 1999)
  Monte Carlo methods to increase the robustness. (S. Thrun, 2000).
  Stop-Scan process for accurate 3D map generation (A. Nüchter, 2007).
Landmarks for error correction
Constructed map

## Slide 9: State of the Art
Algorithms
  Map registration
    Coarse alignment
    Extended Gaussian Image (EGI) Algorithm (A. Makadia, 2006).
    Signature points from curvature (C. Chua, 1997).
    2D Spin image correlation (A. Johnson, 1997).
    Principle component analysis (D. Chung 1998, J. Tarel 1998).
    Fine registration
    Iterative Closest Point (ICP) for fine registration (Bsel, 1992).
    Parallel methods for ICP (C. Langis, 2001).
    Color is applied as filter in ICP (S. Druon, 2006).
  Exploration
    Semantic hierarchy of spatial representation (Kuipers, 1991).
    Greedy strategy. (S. Thrun, 2002).
    Frontier based exploration strategy (B. Yamauchi, 1998).

## Slide 10: 1. Robotic Mapping Systems
3D color mapping system .
Mobile carrier to navigate through given area.
Exploration and mapping process.
Systems
Registration
Analysis
Exploration

## Slide 11: 3D Point Cloud Map Generation
2D LIDAR Scan
3D LIDAR scan using
external rotary actuator
SICK LMS 200 2D LIDAR
2D Light Detection and Ranging-LIDAR: SICK LMS 200.
External rotary actuator used to rotate the LIDAR within a scene.
The position of the rotary actuator is used to create the third dimension.
Systems
Registration
Analysis
Exploration

## Slide 12: Color Mapping Device & Color Point Clouds
θ
φ
2D LIDAR
Motors
Mechanism to register camera image to LIDAR range map
Camera image of urban building
Color range map
Laser reflective intensity range map
Camera
Systems
Registration
Analysis
Exploration

## Slide 13
Remotely Operated and Autonomous Mapping System (ROAMS) *
* B. Gebre, H. Men, K. Pochiraju, “Remotely Operated and Autonomous Mapping System(ROAMS),” IEEE International Conference on Technologies for Practical Robot Applications (TePRA), pp173-178, 2009
Wide angle front bumper video Camera
Birds eye view Pan-Tilt HD video camera with acoustic microphone
Long range wireless communication system antenna
3-DOF video registered LIDAR Scan Systems.
2 Front facing long range (5.5m) IR proximity sensors.
2 Front facing short range (1.5m) IR proximity sensors
4 rear facing long range (5.5m) IR proximity sensors. Running across the width of the vehicle.
On board Quad Core computer (Inside)
Rear facing wide-angle video cameras
Forward facing wide angle Camera (main driving camera)
Systems
Registration
Analysis
Exploration

## Slide 14
Survey Initialization
Spatial Data Acquisition
Complete Surveying
Map integration
Systems
Registration
Analysis
Exploration
Automated Mapping
Initialization
Urban Mapping Process
Traditional mapping process
Robotic exploration and mapping process

## Slide 15: Exploration and Mapping Process
Motivations
1.Initialize global coordinate.
2.Find object in current scene.
3.Determine next observation
position
1. Register into global coordinates.
2. Find missed parts in current scene.
3. Determine next observation position.
1
3
4
2
5

## Slide 16: Stop-Scan Mapping Process
Advantages:
  Use low precision position information.
  Generate accurate global map with low cost.
  Large scale high density point cloud generation.
Sense
Analysis
Plan & Act
Generate point cloud map from mapping device.
Determine next best vantage position to cover unmapped area.
Registration
Register local map into global reference frame.
Identify objects and occlusions, noise filtering, de-sampling.
Systems
Registration
Analysis
Exploration
Notes: Compare different mapping fashions: real-time SLAM mapping (non-accurate landmark mapping)
Stop-scan fashion: non real-time but higher density more accurate map generation.
Mention accurate position sensor is very expensive.

## Slide 17: 2 Point Cloud Analysis
  Noise filtering
  Point cloud surface normal extraction
  Voxel grid based de-sampling
  Occlusion detection in 3D space
  Exploration grid construction
Systems
Registration
Analysis
Exploration

## Slide 18
Systems
Registration
Analysis
Exploration
Noise Filtering
Most of the noise points are outlier points.
Rest of the noise comes from the reflection on dark surface.
Filter performs based on computing point space density d=Np/u.
The points search in unit space is completed based on k-d tree search.
Noise Points
3D Point Cloud with noise
After noise filtering

## Slide 19
Systems
Registration
Analysis
Exploration
Point Surface Normal Extraction
Search k nearest points Pnn{p1,…pk} for point pi.
Fit nearest points set Pnn into a plane Pl.
Computing the plane surface normal npl as surface normal on pi.

## Slide 20
Construct octree on the bounding box of point cloud.
Increase octree level until reaches desired voxel size.
Keep one point in each voxel to ensure the even space distribution.
Systems
Registration
Analysis
Exploration
Voxel De-sampling
Vantage Position
X
Y
Z
Bounding box
1st level octree
2st level octree
Before
After

## Slide 21: Occlusion in Single Vantage Position Map
Blind Areas
Occlusion
Occlusion
Indoor scanned cloud point cloud map with blind areas and occlusions
Systems
Registration
Analysis
Exploration

## Slide 22: How Occlusion Occurs
Occlusions
Scanner blind area
Blind Area
Point cloud data with occlusions
Occluded space
Discontinued edge
Object
Scanned area
Systems
Registration
Analysis
Exploration

## Slide 23: 3D Scan Pattern
Point measurement on 2D scan plane
3D scanner scan pattern
Scan plane
Object surface
Intersection
Laser points
Systems
Registration
Analysis
Exploration

## Slide 24: Occlusion Determination
Occlusion happens when the distance si between the ith point and i+1th point become discontinuous.
Compute a to determine occlusions Apply a=5o as threshold value for occlusion determination
Systems
Registration
Analysis
Exploration
Notes: Delta theta is know from the lidar resolution

## Slide 25: Occlusion Detection Results
Systems
Registration
Analysis
Exploration

## Slide 26: Exploration Grid
Advantages:
  Represent occupancy information about mapping progress.
  Identify obstacles, mapped and unmapped area for exploration.
  Computation cost is reduced from the point cloud processing.
Initialization:
  Utilize given bounding for exploration as boundary of exploration grid.
  Decide grid size based on the characteristics of mapping platform.
  On each grid, determine N elevation levels to describe point distribution.
Update:
  For every point in latest generated point cloud, project them on exploration grid.
  Analyze z distribution pattern to identify objects.
Systems
Registration
Analysis
Exploration
Color Point Cloud
Exploration Grid

## Slide 27: Exploration Grid
Object Identification
  Analyze z-direction point distribution on each grid with known patterns.
  Identify obstacles, ground surface and unmapped area.
Systems
Registration
Analysis
Exploration
Wall
Ground and roof

## Slide 28: 3 Color Point Cloud Registration
  Hue invariance analysis
  Hue assisted color point cloud registration on EGI (coarse registration)
  Hue Assistant ICP (HICP) algorithm (fine registration)
Systems
Registration
Analysis
Exploration

## Slide 29: Point Cloud Registration
Two point clouds (Data & Model) are registered together into a single frame by rigid translation and rotation.
Approach
Set up model and point cloud with their local reference frames.
Rough alignment based on spherical and translational correlation algorithm.
Fine registration with high precision based on Iterative Closest Point (ICP) algorithm.
Data
Model
Systems
Registration
Analysis
Exploration

## Slide 30: Coarse Alignment with
Extended Gaussian Image (EGI) algorithm provides non-iterative solution for point cloud registration.
Point cloud surface normal histogram on Extended Gaussian sphere.
The alignment is determined by maximizing the correlation function between their extended Gaussian Images.
EGI is applied to solve rigid rotation R and translation T.
Rotation alignment is determined before translation alignment.
Stanford bunny point clouds have been applied as benchmark for coarse alignment verification.
EGI of point cloud normal histogram
Systems
Registration
Analysis
Exploration

## Slide 31: Coarse Rotation Alignment
Rotation alignment is targeting to maximize the correlation function about rotation
H1(ω) and H2(ω) are the surface normal histograms on EGI.
ω is the point cloud surface normal vector.
rotation matrix . , SO(3) is a Lie rotation group about origin, R can be described as R=Rz(α)Ry(β )Rz.(γ)
The spherical correlation G(R) is solved in Fourier domain.
.
Systems
Registration
Analysis
Exploration

## Slide 32: Rotation Alignment
Point clouds surface normal are converted into NxN grids EGI.
Rotation alignment is determined by maximizing the correlation function.
Data
Model
EGI of Data
EGI of Model
Systems
Registration
Analysis
Exploration

## Slide 33: Coarse Translation Alignment
Translation alignment is determined by maximizing the correlation function.
F(x) is the occupancy function defined as
is translation vector.
Both model and data point clouds are covered into NxNxN occupancy grids and the correlation is accomplished by selecting the translation to maximize correlation function G.
Systems
Registration
Analysis
Exploration

## Slide 34: Coarse Translation Alignment
Point clouds are converted into NxNxN occupancy grids.
Translation alignment is determined by maximizing the correlation function.
Translation correlation result
Point clouds after translation
Point clouds before translation
Systems
Registration
Analysis
Exploration

## Slide 35: Hue Distribution Analysis
Hue distribution between two color point clouds have been analyzed.
Data
Model
Systems
Registration
Analysis
Exploration
Color point clouds before translation
Hue distribution comparison

## Slide 36: Hue filtered Color Point Clouds
Hue rendered point clouds before registration.
After low pass hue filter (hue<0.5)
Data point cloud
Data point cloud
Model point cloud
Model point cloud
Systems
Registration
Analysis
Exploration

## Slide 37: Hue Constrained Coarse Registration Algorithm
Load data point cloud Pd and model point cloud Pm;
Compute hue on every points in Pd and Pm;
Filter points based on hue distribution;
Filter outlier and voxel de-sampling on both Pd and Pm;
Compute point surface normal nd{1…Nd} on data point cloud Pd and nm{1…Nm} on model point cloud Pm;
Construct orientation histogram Hd and Hm based on extracted point normal;
Solve rigid rotation matrix R by solving the correlation between Hd and Hm with SOFT(3);
Rotate Pd with R, get Pd’;
Building occupancy grid with common bounding box in Pd’ and Pm;
Solving rigid translation T by solving the convolution of Pd’ and Pm,
Save transformed Pd’ for fine registrations.
In which, point pid{xid,yid,zid} in point cloud Pd looks for its nearest neighbor point pim{xim,yim,zim} in point cloud Pm .
Error Measurement
Systems
Registration
Analysis
Exploration

## Slide 38: Hue Constrained Registration Result
Build EGI for alignment.
Registration Result.
EGI of Data
EGI of Model
 | 3D Registration | Hue Constrained
Time (second) | 31.572 | 22.599
Error | 0. 001501 | 0. 001482
Systems
Registration
Analysis
Exploration

## Slide 39: Eight Color Point Cloud Hue Distributions
Systems
Registration
Analysis
Exploration

## Slide 40: Hue Constrained Coarse Registration Performance
Eight Cloud Point Cloud Registered into Global Frame.
Performance is compared with 3D Registration
Systems
Registration
Analysis
Exploration

## Slide 41: Iterative Closest Point Algorithm
Initialize point clouds start position
point association
Rigid transformation computation
Transform data point cloud
Mean square error evaluation
Meets
Stop Criteria?
Registered point cloud data
Y
N
Two 3D color maps are iteratively registered together
Point association happens at every iteration.
Iteration stops after convergence criteria are met.
Pair-wised registration rigidly transforms data 3D map into model 3D map’s coordinates.
Hue assisted algorithm accelerates speed and increases robustness for map registration.
Systems
Registration
Analysis
Exploration

## Slide 42: ICP Algorithm for Fine Registration
Data is registered into model point cloud frame with ICP algorithm.
ICP algorithm is an iterative process that calculates the rigid transformation based on associating two point clouds.
A transformation error function, E(R,T) is defined as the mean distance between associated points.
R and T are the relative 3D rotation and translation.
The point association of correspondence between the data and model point clouds is based on a nearest neighbor search.
The transformation matrix R and T are then updated by minimizing E.
Systems
Registration
Analysis
Exploration

## Slide 43: Points Association Using k-d Tree
K-d tree based closest points association
  K-d tree construction
    Points are inserted into the tree by selecting the median of the subtree.
    The median has been decided sequencing between different dimensions.
  K-d tree closest point range search
    Search algorithm moves down recursively from root node.
    Once search reaches leaf node, leaf node will be considered as candidate.
  K-d tree construction
  K-d tree closest point search
Systems
Registration
Analysis
Exploration

## Slide 44: Introducing Color into ICP
Color point cloud
  Acquired by Vision-Laser Range Finder.
  Provide more detail color information about scanning object.
  Extend point cloud application areas to: object recognition, semantic map building, road detection, etc.
  Increase robustness in point cloud registration.
Comparison between range point cloud and color point cloud
3D Range Point Cloud Scan
3D Color Range Point Cloud Scan
Systems
Registration
Analysis
Exploration

## Slide 45: Selection of the 4th Dimension from Color Data
Red-Green-Blue (RGB) model is easily affected by lighting conditions and view positions.
Camera image at pos #1
Background filtered
Camera image at pos #2
Background filtered
Different colors RGB distributions at 2 positions
Systems
Registration
Analysis
Exploration

## Slide 46: Hue Component Remains Invariant with View Point
Converting RGB into Hue-Saturation-Lightness (HSL) space, hue remains invariant at different view positions.
Different colors hue distributions at pos #1
Different colors hue distributions at pos #2
Systems
Registration
Analysis
Exploration

## Slide 47: Hue Assisted Iterative Closest Point (HICP) Algorithm
Hue assisted ICP algorithm
  Weighed hue value computed as 4th dimension.
  Construct 4D k-d tree.
  4D search in 4D k-d tree produces more accurate pairing.
Rigid transformation matrix computation
  Singular value decomposition
Error evaluation
  Average mean square distance on 3D coordinates
Convergence criteria
  Error value converges;
  Associated points number converges;
  The number of points which changed their paired points compare to previous association goes to 0.
Systems
Registration
Analysis
Exploration

## Slide 48
HICP Methodology
Weighted hue in registration process
  The point association determination on 4D space is based on:
  Both range {x,y,z} and hue h have been normalize to 0~1 range.
  Hue weight is selected between 10% and 35% for accurate association.
Different distributions of hue from the scene affect the registration results.
Registration accuracy can also be measured by normal error.
(e) Position #3potential coverage and travel cost (f) Position #4potential coverage and travel cost
Systems
Registration
Analysis
Exploration

## Slide 49: Benchmark: 6DOF Registration
Urban building color point clouds registration
  Data and model point clouds generation
    Same color point cloud from different vantage point view angle.
    6DOF transformation is known for comparison.
    (Tx= 2.46, Ty=2.612, Tz=0.347, x=0o y=10o, z=10o)
  Point clouds are registered together using HICP
  HICP results have been compared with 3D ICP.
Systems
Registration
Analysis
Exploration

## Slide 50: Benchmark: 6DOF Registration
Systems
Registration
Analysis
Exploration

## Slide 51: Performance with Different Hue Weight and 3D ICP
Systems
Registration
Analysis
Exploration
Methods | Time (seconds) | Iterations
3-DICP | 166.89 | 51
HICP weight=0.05 | 98.05 | 33
HICP weight =0.10 | 93.07 | 30
HICP weight=0.20 | 87.76 | 28
HICP weight=0.40 | 73.11 | 25
HICP weight=1.00 | 56.06 | 21
HICP weight=2.00 | 52.42 | 19
HICP weight=5.00 | 42.25 | 16
HICP weight=10.00 | 36.21 | 14
HICP weight=100.00 | 28.08 | 12
Weight has bee adjusted from 0.05 to 100.00.
Performance area compared in computation time and error.

## Slide 52: Two Different Color Point Cloud Registration with H-ICP
Systems
Registration
Analysis
Exploration
Two color point clouds about indoor scene
Hue rendered point clouds

## Slide 53: Two Different Color Point Cloud Registration with H-ICP
Systems
Registration
Analysis
Exploration
Two color point clouds before and after registration
Before registration
After registration

## Slide 54: Performance Comparison
Systems
Registration
Analysis
Exploration
Methods | Time (seconds) | Iterations | Error | Normal Error
3-DICP | 678.02 | 108 | 0.066 | 0.9957
HICP weight=0.01 | 437.02 | 93 | 0.041 | 0.9968
HICP weight=0.02 | 432.58 | 94 | 0.041 | 0.9969
HICP weight=0.05 | 332.69 | 74 | 0.040 | 0.9969
HICP weight=0.10 | 366.60 | 81 | 0.042 | 0.9969
HICP weight=0.20 | 306.15 | 70 | 0.043 | 0.9971
HICP weight=0.30 | 277.61 | 74 | 0.045 | 0.9971

## Slide 55: Sequential Registration about Unknown Area
Six color point clouds area generated at six vantage positions.
They area pair wisely registered together to evaluation performance.
1
2
3
5
4
6
Systems
Registration
Analysis
Exploration

## Slide 56: Sequential Registration about Unknown Area
Position | 3-D ICP Iteration # | 3-DICP Time(seconds) | HICP Iteration # | HICP Time(seconds) | 3-D ICP Error | HICP Error
2 | 81 | 360.24 | 74 | 263.36 | 0.379 | 0.370
3 | 83 | 203.14 | 37 | 63.43 | 0.303 | 0.301
4 | 84 | 386.54 | 67 | 199.88 | 0.472 | 0.461
5 | 133 | 393.46 | 68 | 329.76 | 0.568 | 0.549
6 | 120 | 465.85 | 71 | 156.69 | 0.947 | 0.849
3D point clouds after registration (pos 2 & pos 3)
Color point clouds after registration (pos 2 & pos 3)
Systems
Registration
Analysis
Exploration

## Slide 57: Case I: 1D Distributed Hue
Point Clouds before Registration
Point Clouds after Registration
1 dimensional assigned hue point clouds registration
  Data and model point clouds generation
    Render bunny point clouds with 7 hue value vary from 0 to 1.
    Hue rendering is based on z value
Color | R | G | B | Hue
Gray | 128 | 128 | 128 | 0
Yellow | 255 | 255 | 0 | 0.167
Green | 0 | 255 | 0 | 0.333
Cyan | 0 | 255 | 255 | 0.5
Blue | 0 | 0 | 255 | 0.667
Magenta | 255 | 0 | 255 | 0.833
Red | 255 | 0 | 0 | 1
Systems
Registration
Analysis
Exploration

## Slide 58: Case I: 1D Distributed Hue
1D distributed hue point cloud registration
  Results have been compared between 3D range data and color rendered 3D range data with range ICP and hue assisted ICP.
  Hue attribute helps to increase ICP speed.
Systems
Registration
Analysis
Exploration

## Slide 59: Case II: Continuous Hue Distribution
Model point cloud
Data point cloud
Registered point cloud
Continuous distributed hue point cloud registration
  Data and model point clouds generation
    Render range point clouds with continuous hue distribution.
    Hue value is ranging from 0 ~ 1.
    Hue value is decided based on z direction coordinate.
Systems
Registration
Analysis
Exploration

## Slide 60: Case II: Continuous Hue Distribution
Continuous distributed hue point cloud registration
  Result is compared with 7 segments hue point cloud.
  Continuous hue point clouds have a better registration performance.
  Hue continuity can effect registration process.
Systems
Registration
Analysis
Exploration

## Slide 61: Case III: Hue Is Noisy
Noise affect on hue assisted ICP
  Data and model point clouds generation
    Render range point clouds with 1D 7 layer hue distribution.
    Random noise on hue has been added with deviation of 50%.
  Noisy point clouds are registered together using hue assisted ICP
Model point cloud
Data point cloud
Registered point cloud
Systems
Registration
Analysis
Exploration

## Slide 62: Case III: Hue Is Noisy
Noise affect on hue assisted ICP
  Noise effect increases registration error.
  Hue attribute increases convergence speed.
Systems
Registration
Analysis
Exploration

## Slide 63: Color Point Cloud Map Example (Indoor / Outdoor) (250+ Million Points, 150 Scans)
Systems
Registration
Analysis
Exploration

## Slide 64: 4. Path Planning for Exploration
  Exploration grid construction and update.
  Heading direction determination.
  Frontier vantage position candidate generation.
  Best view vantage position determination.
Systems
Registration
Analysis
Exploration

## Slide 65: Exploration Grid Update
Exploration grid is generated from the point cloud based on z-directional point distribution.
Exploration grid describe objects as unmapped area (U), ground surface (G) and obstacles/walls (O).
The exploration grid can be updated by:

## Slide 66: Heading Direction Computation
Exploration grids are utilized to computed heading direction for next step movement.
Heading direction H is defined by a force field that attracted by unmapped area and repulsed by the obstacles surface.
The attraction scale factor KkI increases with the distance between unmapped grids and current location. The repulsive scale factor KlI is high for walls that are close by current location.

## Slide 67: Vantage Position Generation
Heading direction is utilized to determine the field of frontier detection.
The frontier positions is detected based on accessibility by A* algorithm.
Frontier positions are generated for next vantage position determination.
Systems
Registration
Analysis
Exploration
H=[-0.9963 -0.0856]
Heading direction provide frontier search field
Generated frontier candidate positions

## Slide 68: Next vantage position Determination
Computing coverage area based on the LIDAR range.
Determine potential coverage area by considering current known obstacles.
Determine the next vantage position from candidate positions Pci who has largest potential coverage area.
Systems
Registration
Analysis
Exploration
Frontier position coverage area
Frontier position coverage area considering obstacles

## Slide 69: Path Planning for Exploration and Mapping
Methodology:
  Heading direction calculation based on obstacles and unmapped space.
  Frontier exploration strategy to generate candidate vantage positions.
  Traversable determination based on A* path planning algorithm.
  Next vantage determination from the candidate positions who has largest coverage of unmapped area.
Evaluation:
  Occupancy grids of mapping area for map completeness evaluation.
  Exploration grid ensures all point density on object surface meet requirement of CAD model extraction.

## Slide 70: Exploration and Mapping Result

## Slide 71: Concluding Remarks
Design and prototyping the hardware
  A mobile robotic platform was designed and built with four-wheel driven all-terrain vehicle.
  Stationary 3D scanner was developed for color 3D mapping purpose.
Scan-Stop-Scan methodology for autonomous exploration mapping
  No precise location sensor is used and the scan registration depends upon the scene continuity.
  The number of stops required by the vehicle depends upon the scanner range
Point Cloud Analysis
  Occlusion detection in 3D space based on depth discontinuity.
  Point cloud processing with noise filter, voxel de-sampling, normal extraction.
  Construction and update of exploration grid from point clouds.
  Identify obstacle and ground surface on exploration grid.
Notes: Highlight contributions after proposal

## Slide 72: Concluding Remarks
Color point cloud map registration algorithm
  Coarse registration algorithm has been developed to roughly align point clouds together. Hue is utilized as a filter to assist registration process and increase the performance.
  Fine registration algorithms have been developed to register observed point cloud map together.
  Color property has been introduced into the registration process for accelerating the speed and increasing the robustness.
Path planning strategy for exploration and mapping
  Heading direction computation based on force field.
  Frontier extraction on exploration grid.
  Potential coverage estimation on exploration grid.
  Next vantage position determination based on coverage of unmapped area.
Notes: Highlight contributions after proposal

## Slide 73: Future work
  Integrating hue into EGI construction process
    Weighted hue value can also be combined together with normal histograms to increase the coarse registration process.
  Object Surface and Contour Identification.
    Surface reconstruction can be completed based on the point cloud analysis result.
  Optimization of exploration strategy and map evaluation.
    The exploration strategy can be evaluated to optimize trajectory of the exploration process.